## Slide 1: Fall from Heights Fatalities Analysis Prepared for the Chief Prevention Officer
December 2018

## Slide 2: Project Overview
The project was undertaken to better understand causes (“contributing factors”) and circumstances around falls from heights.
It involved reviewing and extracting information from files prepared by ministry inspectors about fatal injuries to better understand contributing factors.
This included a review of 92 fall from height fatality events that occurred from 2009 to 2016 (excludes slips, trips, staircases).

## Slide 3: Limitations
Sample Size: The small sample size (n=92) limits the explanatory power of the analysis
Only Fatalities: The analysis covers only fatalities, not not-fatal injuries. The conditions and factors surrounding critical injuries may be similar to or different than those that lead to fatalities.
Data Quality: Data source contained information that is relevant only to the specific event information relevant for analysis had to be extracted/interpreted from the event details. Additionally, not every data point was available in every file.
Data Capture, Coding and Interpretation: Despite the rigorous consistency checks, there might have been differences in coding and interpreting the information by the team working on the pilot project.

## Slide 4: Results: Overview

## Slide 5: Fatalities by Region and Program
60 fatalities occurred in construction workplaces that are under the program authority of CHSP (65.2%).
26 fatalities occurred in the Central East (28.3%) and 23 in Central West (25.0%) regions.
One fatality occurred in a workplace that is under the program authority of Healthcare Unit.
 | Program |  |  | 
Region | CHSP | IHSP | HCU | Total
Central East | 17 | 9 | 0 | 26
Central West | 15 | 8 | 0 | 23
West | 15 | 6 | 0 | 21
East | 9 | 6 | 1 | 16
North | 4 | 2 | 0 | 6
Total | 60 | 31 | 1 | 92

## Slide 6: Fatalities by Year
The year-to-year fall-from-heights fatality numbers show a slight downward trend. However, the number of annual fatalities is subject to year-to-year fluctuations and a high degree of variation, limiting the ability to draw statistically meaningful trends on an annual basis.
The overall trend of fall-from-heights fatalities was similar to the trend for all traumatic fatalities.
Chart: Year of Death
| 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
Falls from Height | 14 | 16 | 11 | 8 | 15 | 8 | 13 | 7
All Fatalities | 47 | 56 | 55 | 39 | 65 | 55 | 50 | 47


## Slide 7: Fatalities by Month
Fatality trend had a spike during summer months, a sharp decline in September, and remained relatively high through December.
Due to the small sample size, the sharp decline in September might not be statistically relevant. Nevertheless, it can be said that falls fatalities increased in summer months when construction activity was high.
Chart: 
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Total | 5 | 6 | 5 | 6 | 4 | 8 | 12 | 15 | 3 | 10 | 8 | 10

## Slide 8: Fatalities by Time of Day
The number of fatalities began to increase around 9 a.m., declined around 12 noon, and spiked around 2 p.m., after which it diminished gradually.
The decline around 12 p.m. can be attributed to low work activity during lunch break.
*Event time was rounded to the nearest hour.
Chart: 
| 7 AM | 8 AM | 9 AM | 10 AM | 11 AM | 12 PM | 1 PM | 2 PM | 3 PM | 4 PM | 5 PM | 6 PM | 7 PM | 8 Pm | 9 PM | 10 PM | 11 PM
 | 3 | 1 | 6 | 9 | 11 | 5 | 9 | 13 | 9 | 8 | 6 | 5 | 3 | 2 | 0 | 1 | 1

## Slide 9: Fatalities by Age Group
The 45-54 age group had the highest number of fatalities (26.1%), followed by the 35-44 age group (21.7%).
There were 8 fatalities among “young workers”—those who are under the age of 25 (8.7%).
There were 9 fatalities among those 65 and older (9.8%).
Chart: Age Group
| 15-24 | 25-34 | 35-44 | 45-54 | 55-64 | 65+
Total | 8 | 15 | 20 | 24 | 16 | 9

## Slide 10: Fatalities by Industrial Sector
Industrial sector information (by The North American Industry Classification System or NAICS 5-digit) was available in the case of 60 of the fatalities.
The industrial sector category with highest number of fatalities was “Roofing contractors” (21 fatalities, 22.8%), followed by the residential building construction” (13 fatalities, 14.1%)
“Arborists” accounted for 3 of the 7 “landscaping services fatalities”.
Chart: Top 10 NAICS (5-Digit) by Fatalities (n=60)
| Plate work and fabricated structural product manufacturing | Other building equipment contractors | Poured concrete foundation and structure contractors | Finish carpentry contractors | Plumbing, heating and air-conditioning contractors | Supermarkets and other grocery (except convenience) stores | Masonry contractors | Landscaping services | Residential building construction | Roofing contractors
Total | 2 | 2 | 2 | 2 | 3 | 3 | 5 | 7 | 13 | 21

## Slide 11: Injured Worker – Time in Role
29 workers had been in their role for less than one year.
Chart: Fatalities by Time in Role (n=64)
| 0 | 1 | 2 | 3 | 4 | 6 | 7+
Total | 29 | 8 | 4 | 6 | 3 | 5 | 9

## Slide 12: Time in Role
The chart above provides the breakdown of the 29 workers who had died in their first year on the job.
A cumulative count reveals that 14 workers died in their first month
  7 of those workers died in their first week
  3 of those workers died on their first day

## Slide 13: Experience
This chart highlights that information about worker experience is inadequate in the files. The experience level of the worker is unknown in 40 fatalities or in 48.8% of the analyzed cases.
21 of the workers had been in the same line of work for over 10 years.
Inexperienced (<1 year)
Inexperienced (1-3 years)
Highly Experienced (3-10 years)
Veteran (10+ years)
Chart: Fatalities by Experience
| Unknown | Inexperienced | Experienced | Highly Experienced | Veteran
Total | 40 | 12 | 8 | 11 | 21

## Slide 14: Height of Fall
The most common height of fatal falls was from 6 metres (16 fatalities) Fatal falls from 3 metres was nearly as common (14 fatalities). These heights roughly correspond to two-storey and one-storey roof/floor heights.
12 fatal fatalities were from a height of less than 3 metres.
The four fatal falls that were from 60 metres were due to the same incidence.
Chart: Number of Fatalities by Height of Fall (n=89)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 16 | 21 | 25 | 27 | 31 | 40 | 60 | 75
Total | 3 | 9 | 14 | 8 | 7 | 16 | 3 | 5 | 4 | 1 | 2 | 3 | 2 | 1 | 2 | 1 | 1 | 1 | 1 | 4 | 1

## Slide 15: Worker Location and Height of Fall
 | Height (m) |  |  |  |  |  |  |  |  |  |  | 
Worker Location | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10-19 | 20+ | Total
Roof |  |  | 4 | 3 | 2 | 9 | 2 | 3 | 1 | 4 |  | 28
Ladder | 1 | 7 | 1 | 1 | 4 | 3 | 1 |  | 1 |  | 2 | 21
Scaffold |  | 1 | 3 | 1 |  | 2 |  |  |  | 1 |  | 8
Suspended Platform |  |  |  |  |  |  |  |  |  | 1 | 6 | 7
Floor |  |  | 4 | 1 |  |  |  |  |  | 1 |  | 6
Moving Equipment | 1 |  | 2 |  |  | 1 |  |  | 1 |  |  | 5
Other |  |  |  | 1 |  | 1 |  | 1 |  |  | 1 | 4
Tree |  |  |  |  |  |  |  | 1 | 1 | 1 |  | 3
Road/Ramp/Dock | 1 |  |  |  | 1 |  |  |  |  |  | 1 | 3
Balcony |  |  |  |  |  |  |  |  |  | 1 | 1 | 2
Platform |  | 1 |  | 1 |  |  |  |  |  |  |  | 2
Total | 3 | 9 | 14 | 8 | 7 | 16 | 3 | 5 | 4 | 9 | 11 | 89
31.5% of the fatal falls were from roofs (28 fatalities). Nine of these roof falls were from 6 metres.
Ladders accounted for 23.6% of fatal falls (21 fatalities). Seven of these ladder falls were from 2 metres.
There were six fatal falls from suspended platforms that were more than 20 metres.
Worker location was rolled up to a less detailed level and some heights were grouped. Note that fatalities for which heights were unknown were excluded.

## Slide 16: Worker Location Details
The most common fall location was roof edge (20 fatalities) followed by ladder (19 fatalities).
Worker location is further divided by the nature of fall. For example, the breakdown of the 29 of fatal falls from roofs was as follows: roof edge 20, through skylight 5, and through roof 4.
Note: 29 of fatal falls from roofs includes 1 fatality with unknown height.
Chart: Fatalities by Worker Location (n=92)
| Roof Edge | Ladder | Scaffold | Suspended Platform | Through Skylight | Through Roof | Through Floor | Tree | Balcony | Forklift | Ladder - Extension | Platform | Tower (Antenna) | Road | Truck (Boom) | Unknown | Loading Dock | I-Beam | Parking Garage Ramp | Truck (Pickup) | Truss | Through Gap | Floor Edge | Gantry | Scissor Lift
Total | 20 | 19 | 8 | 7 | 5 | 4 | 4 | 3 | 3 | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 17: Number of Workers on Worksite
63.4% of the fatal falls (52 fatalities) occurred on the worksites where there were 1-3 workers present at the time of the incident
This might be due to small projects’ relative lack of formality and training compared to larger operations.
Chart: Fatalities by Number of Workers on worksite (n=82)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 10 | 19 | 20 | 26 | 30 | 52 | 75
Total | 14 | 23 | 15 | 5 | 6 | 2 | 2 | 3 | 6 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 18: Company Size
The previous slide showed that most workers were working alone or in small groups at the time of the fatal fall.
This slide makes a similar point, this time on company size: Small businesses accounted for most of the fatalities. The businesses with 1-5 workers accounted for 48.9% of fatal fall (45 fatalities).
Chart: Fatalities by Company Size (n=92)
| 1 - 5 | 6 - 19 | 20 - 49 | 50+ | Unknown
Total | 45 | 20 | 7 | 14 | 6

## Slide 19: Results: Contributing Factors

## Slide 20: Contributing Factor Methodology
A contributing factor is defined as an issue pertinent to a fall, which may not have caused the fatality alone or directly, but whose presence increased the likelihood of a fall.
A list of 13 contributing factors based on common hazards and themes was produced.
The 92 fatalities were then reviewed and assigned relevant factors.
Each fatality had anywhere between 1 and 6 factors.

## Slide 21: List of Factors
Factor | Description
Not Wearing PPE | No PPE (e.g. fall arrest harness) was worn by worker as required
Wearing PPE Improperly | Worker wore PPE incorrectly
Lack of Falls Training | Worker did not have any fall specific training
Lack of Worksite Instruction | Worker did not receive training or instruction specific to their worksite and its hazards
Unsafe Behavior/Misjudgment | Worker knowingly behaved in an unsafe manner or misjudged a clear hazard
Overexertion and Unusual Control | Incident caused by worker fatigue or impairment
Pushed or Struck by Object | Worker hurt or made to fall by object
Improper Guarded | Missing or improperly installed guarding such as guardrails (balcony, opening), skylights or hole covering
Unsafe Ladder Use | Ladder used inappropriately
Unsafe Scaffold | Scaffold used inappropriately
Other Unsafe Tools/Equipment or Usage | Tools and equipment (non-ladder or scaffold) used inappropriately
Harmful Conditions | Worksite conditions such as weather, noise or cluttered floorspace

## Slide 22: Contributing Factors: Summary Results
“Lack of worksite instruction” was the most common contributing factor. It was observed in 44 of the 92 fall fatalities (47.8%).
“Not wearing PPE” was a contributing factor in 42.4% of the fatalities, “lack of falls training” in 31.5%, “wearing PPE improperly” in 26.1%, and “improper guarding” in 23.9%.
Chart: Contributing Factors
| Overexertion and Unusual Control | Pushed or Hurt by Object | Unsafe Scaffold | Unsafe Behaviour/Misjudgement | Other Unsafe Tools/Equipment or Usage | Unsafe Ladder Use | Harmful Conditions | Improper Guarding | Wearing PPE Improperly | Lack of Falls Training | Not Wearing PPE | Lack of Worksite Instruction
Total | 7 | 7 | 7 | 12 | 13 | 16 | 17 | 22 | 24 | 29 | 39 | 44

## Slide 23: Focus: PPE and Age
Chart: Top 5 Factors by Age
| 15-24 | 25-34 | 35-44 | 45-54 | 55-64 | 65+
Wearing PPE Improperly | 4 | 7 | 7 | 5 | 1
Not Wearing PPE | 2 | 6 | 9 | 8 | 8 | 6
The 55-64 and 65+ age brackets indicate that PPE is more often not worn as opposed to worn incorrectly.
This is in contrast with the younger age groups.
Notes: Factor analysis by age is shown for Top 5 factors. Note that as there are multiple factors that lead to a fatality, this analysis has been done on factors by age groups and is not about fatality by age group

## Slide 24: Focus: PPE and Age.
For the older age groups, not wearing PPE was a more common factor than wearing PPE improperly.
  Not wearing PPE was a factor in 6 of 9 fatalities that occurred in the 65+ age group.
  Wearing PPE improperly was a factor in only 1 of the 16 fatalities that occurred in 55-64 age group.
For the younger age groups, wearing PPE improperly was more common.
  Wearing PPE improperly was a factor in 4 of the 8 fatalities that occurred in the 15-24 age group (“young workers”)
Age Group | Number of Fall Fatalities in the Age Group | Fatalities where "Not Wearing PPE" was a factor | Fatalities where "Wearing PPE Improperly" was a factor
15-24 | 8 | 2 (25.0%) | 4 (50.0%)
25-34 | 15 | 6 (40.0%) | 7 (46.7%)
35-44 | 20 | 9 (45.0%) | 7 (35.0%)
45-54 | 24 | 8 (33.3%) | 5 (20.8%)
55-64 | 16 | 8 (50.0%) | 1 (6.3%)
65+ | 9 | 6 (66.7%) | 0 (0.0%)
Total | 92 | 39 (42.4%) | 24 (26.1%)
Notes: Factor analysis by age is shown for Top 5 factors. Note that as there are multiple factors that lead to a fatality, this analysis has been done on factors by age groups and is not about fatality by age group

## Slide 25: Factor Analysis – By Industrial Sector
Lack of worksite instruction is the most common factor in both construction and non-construction sectors (based on the 2-digit NAICS)
  “Lack of worksite instruction” was a factor in 47.5% of 61 fall fatalities in construction sectors and 46.4% of 31 fatalities in the sectors other than construction.
  “Harmful conditions” ” was a factor in 14.8% of 61 fall fatalities in construction sectors and 25.8% of 31 fatalities in the sectors other than construction.
Chart: Top 7 Factors for Construction and non-Construction
| Non-Construction | Construction
Lack of Worksite Instruction | 15 | 29
Not Wearing PPE | 12 | 27
Lack of Falls Training | 9 | 20
Wearing PPE Improperly | 4 | 20
Improper Guarding | 7 | 15
Harmful Conditions | 8 | 9
Unsafe Ladder Use | 7 | 9

## Slide 26: Training: Notes
For the purpose of this analysis, “Falls Training” represents a mention in the file that the worker took some type of falls prevention training.
There was no information/supporting documents found to assess the quality of the training.
It’s not possible to draw conclusions from this study about the effectiveness of the Working at Heights (WAH) training.
  This analysis covered the falls fatalities that occurred from 2009 to 2016. The mandatory WAH training program standard came into force in April 2015. In specific circumstances, some employers also had until October 2017 to ensure workers completed the working at heights training offered by the approved training providers.

## Slide 27: Training
37 workers had falls training (40%), 29 workers did not (32%). Training information was not included in 26 of the analyzed cases (28%).
Among the 61 construction* fatalities analyzed:
  32 workers had falls training (52.4%), 20 didn’t receive training (33%), training information was not available in 9 of the analyzed construction fatalities (14.7%).
Among the 31 non-construction* fatalities analyzed:
  5 workers had falls training (16%), 9 didn’t receive training (29%), training information was not available in 17 of the analyzed construction fatalities (55%).
Chart: 
| Construction | Non-Construction
No Falls Training | 20 | 9
Falls Training | 32 | 5
*Note: 2-digit NAICS was used to define Construction or Non-Construction sectors.

## Slide 28: What Went Wrong Despite Training
Of the 37 workers who had some form of falls training:
  28 had issues with PPE: 16 worn PPE improperly and 12 did not wear it at all.
  13 workers did not receive adequate worksite instruction.
Chart: Factors Present When Falls Training is Evident
| Overexertion and Unusual Control | Harmful Conditions | Unsafe Scaffold | Unsafe Ladder Use | Pushed or Hurt by Object | Unsafe Behaviour/Misjudgement | Other Unsafe Tools/Equipment or Usage | Improper Guarding | Not Wearing PPE | Lack of Worksite Instruction | Wearing PPE Improperly
Total | 2 | 2 | 3 | 3 | 4 | 4 | 6 | 9 | 12 | 13 | 16

## Slide 29: Highlighted Contributing Factors by Business Size
1-5 Employees | 6-19 Employees
Pushed or Struck by Object (6/7) Of 7 fatalities involving this factor, 6 were of workers who worked for businesses with 1-5 employees. | Other Unsafe Tools/Equipment or Usage (7/13) Of 13 fatalities involving this factor, 7 were of workers who worked for businesses with 6-19 employees.
Unsafe Scaffold (6/7) | 
Unsafe Ladder Use (9/13) | 
Unsafe Behavior/Misjudgment (8/10) | 
Lack of Falls Training (17/29) | 
Not Wearing PPE (22/36) | 
No factors were specifically notable for businesses of size 20-49 or 50+.
Notes: The total fatalities in small business (size 1-5) was 45 out of 92 that were analyzed

## Slide 30: Highlighted Contributing Factors by Top 2 Industrial Sectors (NAICS 5 Digit)
Roofing Contractors | Residential Building Construction
Lack of Worksite Instruction (10/21) (10 out 21 fatalities in “roofing contractors” sector involved this factor) | Lack of Worksite Instruction (9/13) (9 out 13 fatalities in “residential building construction” sector involved this factor)
Not wearing PPE (10/21) | 
Wearing PPE Improperly (9/21) | Wearing PPE Improperly (7/13)
Improper Guarding (7/21) | 
 | Lack of Falls Training (6/13)
Notes: The total fatalities in small business (size 1-5) was 45 out of 92 that were analyzed

## Slide 31: Summary

## Slide 32: Summarized Takeaways
The year-to-year fall-from-heights fatality numbers show a slight downward trend. However, the number of annual fatalities is subject to year-to-year fluctuations and a high degree of random variation, limiting the ability to draw statistically meaningful trends on an annual basis.
Fatality numbers had a spike during summer months, a sharp decline in September, and remained relatively high through December.
The number of fatalities begins to increase around 9 a.m., declines around 12 noon, and spikes around 2 p.m., after which it diminishes gradually.
Fatalities by age are distributed in a bell curve with nearly equal occurrence in the 15-24 (“young workers”) and 65+ age groups.
Roofing contractors and residential building construction were the most common industrial sectors (NAICS 5-digit).
29 workers were in their current role less than 1 year.
14 workers had been on the job less than 1 month.

## Slide 33
While workers time in role and experience were positively correlated, there was a significant number of fatalities where the worker had experience, but was fairly new to their current job.
Workers fell from as little as less than a meter, but the most common heights of fatal falls were from 3 and 6 metres. These heights roughly correspond to one and two-storey heights.
The two most common locations that workers fell from were roof edges and ladders.
Most fatalities occurred on the worksites where there were 1-3 workers present at the time of incident
Most workers worked for businesses with 1-5 employees.
The three most common contributing factors to falls were lack of worksite instruction, not wearing PPE and lack of falls training.

## Slide 34
For the older age groups, not wearing PPE was a more frequent factor than wearing PPE improperly. Whereas wearing PPE improperly was more frequent for the younger age groups.
A lack of worksite instruction is the most common factor in fatal falls in construction and non-construction sectors.
About half of construction fatalities involved workers who had falls training.
Of these 32 construction* related fatalities of workers who had falls training, the most common factors were wearing PPE improperly, lack of worksite instruction, and not wearing PPE.
Small businesses featured a larger proportion of the following factors: pushed or struck by object, unsafe scaffold, unsafe ladder, unsafe behavior/misjudgment, lack of falls training and not wearing PPE.
Roofing contractors and residential building construction were the NAICS (5 digit) with the most number of fatalities and had large than average instances of lack of worksite instruction and wearing PPE improperly.
*Note: 2-digit NAICS was used to define Construction sectors.